## Slide 1
Oriol Colomés
Week 5. Modal analysis

## Slide 2: Learning objectives
At the end of this week you will be able to:
Define numerical methods to perform a modal analysis of systems governed by Partial Differential Equations. This entails:
  Characterize the modal properties of a system of PDEs
  Define numerical methods that return characteristic eigenfrequencies and eigenmodes of a system of PDEs
  Analize and justify the results

## Slide 3
Introduction to modal analysis
5.1

## Slide 4: What is modal analysis?
An operation from which we can calculate intrinsic properties of the system.
In the context of dynamic structural analysis, these are:
      Natural frequencies
      Natural shapes of vibration
The natural frequencies correspond to the frequencies at which the structure responds, when moved from its resting position and then released (ultimately finding the equilibrium again).
The natural shapes of vibration correspond to deformed mode of the freely vibrating structure at each of the natural frequencies.
The modal properties (frequencies and shapes) can be used to assess about the suitability of the constructed model.

## Slide 5: What is modal superposition?
An operation that consists in calculating the structural response by superposing the response of each natural vibration mode. How does it work?
It relies on superposition of responses, and thus it is valid only for linear (or linearized) systems.
      The response of each mode (modal response) can be calculated independently of the others, as if it was a SDOF system
      The response of the structure is obtained by adding the modal responses

## Slide 6: Why would we use modal superposition?
The modal response of each mode is obtained in the same way as a SDOF system (“easy” and fast: solving coupled differential equations is “more difficult”/slower than solving a normal ODE)
Most of the times, not all modes need to be included in the response for it to be accurate (modal reduction), saving time in this way
The highest modes require smaller time steps for convergence, if explicit methods are used - Euler stepping method or Runge-Kutta (ODE45). Not including them, we can get away with larger time steps, thus saving time
The highest frequency modes are the least accurate in any case, so it is okay to exclude them.

## Slide 7
Modal Orthogonality
5.2

## Slide 8: Modal properties
If the structure is at least isostatic, then is positive definite and all eigenvalues are positive. Otherwise, some eigen frequencies are null, which correspond to rigid body motions.
Some properties of the modal basis (number and dimensions/ values of , orthogonality):
All eigenvalues are real (because and are (semi-)positive definite)
There are as many eigen pairs (,) as there are equations (dimensions of matrices and ). The modal shapes have as many components as the dimensions of and .
The eigen shapes (modal shapes) are linearly independent, and stiffness and mass orthogonal, i.e.,

## Slide 9: Modal orthogonality
Exercise: Proof that the eigenvectors are and -orthogonal
Hints:
Write the modal equation for two distinct eigenvalues, i and j
Multiply first line by and second by
Use the symmetry of matrix and

## Slide 10: Modal orthogonality
Use the orthogonal properties of the modal shapes to uncouple the equations
Write the equations of motion (FEM, DEM, any other method)
Calculate the eigenshapes (free dofs only)

## Slide 11: Modal orthogonality
Use the orthogonal properties of the modal shapes to uncouple the equations
Write the solution as a combination (superposition) of the modal shapes
Replace and in the equation of motion
Left multiply by

## Slide 12: Modal orthogonality
Use the orthogonal properties of the modal shapes to uncouple the equations

## Slide 13: Modal orthogonality
Use the orthogonal properties of the modal shapes to uncouple the equations

## Slide 14: Modal orthogonality
Use the orthogonal properties of the modal shapes to uncouple the equations

## Slide 15: Modal orthogonality
Use the orthogonal properties of the modal shapes to uncouple the equations

## Slide 16
Modal superposition in damped systems
5.3

## Slide 17: Modal superposition for damped systems
Replace , and by the corresponding modal summations, and multiply by
What happens when we add damping?

## Slide 18: Modal superposition for damped systems
What happens when we add damping?
Is the matrix diagonal?
????????
NO. For generic matrix C, the transformed matrix is not diagonal, meaning that the equations cannot be uncoupled in this way.

## Slide 19: Modal superposition for damped systems
What happens when we add damping?
However, it is common practice to define damping in such a way that the resultant transformed matrix is diagonal:
Rayleigh damping
Modal damping

## Slide 20: Rayleigh damping

## Slide 21: Modal damping ratio
In this approach, we define damping associated with each mode shape, usually as a percentage of the critical damping:
If we want to retrieve the damping matrix:
This is very rarely necessary!

## Slide 22: Raleigh damping vs Modal damping ratio
Modal damping ratio:
Rayleigh damping:

## Slide 23
Initial conditions
5.4

## Slide 24: Initial conditions in modal superposition
The unknowns of the resulting system are modal shapes. We cannot use the physical displacement, velocity and acceleration fields directly! 
For us to be able to solve it, we still need to define initial conditions for each of the modal responses:
Uncoupled system of equations:

## Slide 25: Initial conditions in modal superposition
How?

## Slide 26: Initial conditions in modal superposition
What about velocities?
Initial modal displacement
Initial modal velocity
Exactly the same process….

## Slide 27: The final modal superposition recipe
Calculate the mass and stiffness matrices (K, M) of your system (FEM, FD, …)

## Slide 28: Thank you for your attention
Oriol Colomés