## Slide 1: Automation vs Orchestration …what’s the deal?
Simone Spinelli
Network Architect @GÉANT
<simone.spinelli@geant.org>

## Slide 2: Before we begin…
This is our experience and our reasons: we are here to share and listen.
There is no silver-bullet, no recipe, no magic
It’s hard however you approach this
We would be very happy to hear your story and thoughts.

## Slide 3: Why network automation (...just in case)
`
Consistency:
  We noticed that config that should be the same across the whole estate is not.
  Services that should behave consistently are not
Preventing mistakes:
  Imagine if I copy and paste: 192.168.0.1/31
Cosmetics:
  WheN_I_sEE_this | IT_REALLy | hurTS_my_ey3s
Avoid reverse engineering all the time:
  How is this supposed to work?
  Why is this firewall filter present?
Speed, predictability:
  We started this last week, but then an optic was broken, and we had to wait for replacement… now I should start again from scratch.
  Oh no! I forgot to update DNS!
  Oh no! someone forgot to remove a static route somewhere!

## Slide 4: We should do something about it…

## Slide 5: And so it starts…

## Slide 6: Missing the forest for the tree…
What do we really want:
  Sleep at night…
  A network that adhere to our design
  Be aware of exceptions
  Be fast in adapting our design
  Simple interfaces: that guides us instead of confusing us
  Meaningful, understandable, accessible data

## Slide 7: Two interconnected worlds
Processes:
What is the service and how do you deliver it?
Who decides? And how?
What is the authoritative system for a specific data?
Anything else that must happen because of your action?
Artifacts:
Is it config?
What is static/design?
What depends from the single instance?
Where is the data coming from?
What are the possible variants?

## Slide 8: Two interconnected worlds
Processes:
What is the service and how do you deliver it?
Who decides? And how?
What is the authoritative system for a specific data?
Anything else that must happen because of your action?
Artifacts:
Is it config?
What is static/design?
What depends from the single instance?
Where is the data coming from?
What are the possible variants?
Orchestration
Represent the business logic
Interacts with multiple systems
Agnostic to the context
Generally, end-to-end
Typically, where we want to be
Automation
Executes atomic actions:
  Push some config
  Gather data
  Execute something
Highly specialized, dependent from the context (Cisco/Juniper/Nokia/Linux/*)
The focus is the artifact itself
Typically, where we all start

## Slide 9: What’s my point?
Analyze & rethink our processes
Node decomposition
Service decomposition
Config decomposition
Approaching top to bottom (Orchestration) has been a winning choice for us.
“Shift our thinking from lines of config to abstract models”

## Slide 10: Processes

## Slide 11: Decomposition
What are routers made of?

## Slide 12: Decomposition
What are routers made of?

## Slide 13: Decomposition
What are routers made of?

## Slide 14: Config decomposition
neighbor 1.2.3.4 {
description "-- Peering with SURF --";
accept-remote-nexthop;
out-delay 10;
import [ ps-BOGONS ps-RPKI-RE-PEER ps-from-SURF1-nren ];
authentication-key "$@$%DGKND#$%^#^%$"; ## SECRET-DATA
export [ ps-BOGONS ps-to-SURF1-nren ];
peer-as 1103;
bfd-liveness-detection {
minimum-interval 3000;
multiplier 3;
}
}

## Slide 15: This is design
neighbor 1.2.3.4 {
description "-- Peering with SURF --";
accept-remote-nexthop;
out-delay 10;
import [ ps-BOGONS ps-RPKI-RE-PEER ps-from-SURF1-nren ];
authentication-key "$@$%DGKND#$%^#^%$"; ## SECRET-DATA
export [ ps-BOGONS ps-to-SURF1-nren ];
peer-as 1103;
bfd-liveness-detection {
minimum-interval 3000;
multiplier 3;
}
}

## Slide 16: This is specific for that Organization/Partner
neighbor 1.2.3.4 {
description "-- Peering with SURF --";
accept-remote-nexthop;
out-delay 10;
import [ ps-BOGONS ps-RPKI-RE-PEER ps-from-SURF1-nren ];
authentication-key "$@$%DGKND#$%^#^%$"; ## SECRET-DATA
export [ ps-BOGONS ps-to-SURF1-nren ];
peer-as 1103;
bfd-liveness-detection {
minimum-interval 3000;
multiplier 3;
}
}

## Slide 17: This is specific for that instance
neighbor 1.2.3.4 {
description "-- Peering with SURF --";
accept-remote-nexthop;
out-delay 10;
import [ ps-BOGONS ps-RPKI-RE-PEER ps-from-SURF1-nren ];
authentication-key "$@$%DGKND#$%^#^%$"; ## SECRET-DATA
export [ ps-BOGONS ps-to-SURF1-nren ];
peer-as 1103;
bfd-liveness-detection {
minimum-interval 3000;
multiplier 3;
}
}

## Slide 18: This is an additional feature
neighbor 1.2.3.4 {
description "-- Peering with SURF --";
accept-remote-nexthop;
out-delay 10;
import [ ps-BOGONS ps-RPKI-RE-PEER ps-from-SURF1-nren ];
authentication-key "$@$%DGKND#$%^#^%$"; ## SECRET-DATA
export [ ps-BOGONS ps-to-SURF1-nren ];
peer-as 1103;
bfd-liveness-detection {
minimum-interval 3000;
multiplier 3;
}
}

## Slide 19: From config to models
neighbor {{ neighbor.ipv4_address }} {
description "-- Peering with {{org.name}} --";
accept-remote-nexthop;
out-delay 10;
import [ ps-BOGONS ps-RPKI-RE-PEER {{ org.import_policy }} ];
authentication-key ”{{ neighbor.auth_key }}"; ## SECRET-DATA
export [ ps-BOGONS {{ org.export_policy} } ];
peer-as {{ org.as_number }};
{% if neighbor.features.bfd_enable == True %}
bfd-liveness-detection {
minimum-interval {{ bfd.minimum_interval }};
multiplier {{ bfd.multiplier }};
}
{% endif %}
}

## Slide 20: From config to models
So, in the end we have 2 constructs:
Neighbor: Represent a BGP peering session
  Address: ipv4 address
  Authentication_key: string
  Features:
    BFD: boolean
Org: Represent the other side of the cable
  Name: string
  AS_number: int
  Import_policy: list(dicts)
  Export_policy: list(dicts)

## Slide 21: WFO
In WorkflowOrchestrator works the same:
We think in terms of products: a composition of product blocks
Product blocks are abstract objects that have attributes
An instance of a product, instantiated for someone is a subscription.
Workflows manipulate the subscription modifying the lifecycle state

## Slide 22: Ok, but where is the data coming from?

## Slide 23: Source(s) of truth

## Slide 24: Source(s) of truth
…BUT NOT IN THE NETWORK

## Slide 25: Architecture and design
The word “architecture” is often used in the context of something at a high level that is divorced from the lower-level details, whereas “design” more often seems to imply structures and decisions at a lower level. But this usage is nonsensical when you look at what a real architect does.
…
In short, I see all the little details that support all the high-level decisions. I also see that those low-level details and high-level decisions are part of the whole design of the house.
And so it is with software (network) design. The low-level details and the high-level structure are all part of the same whole.
Clean Architecture: A Craftsman's Guide to Software Structure and Design
Robert C. Martin

## Slide 26: Sources of truth
Different ”point of view” means different system (SoTs)
  IP allocation is a different point of view compared to interface allocation
  Firewall filters and routing policies must be adapted to vendor’s dialect
  Different vendors might need to behave differently to give you what you want
The main source of truth is design.
  Design is everywhere: in my models, in my templates, in my workflows.
WFO is there to keep them all in sync
  Design is the sum of all these parts, and more.
  A good modeling gives you the ability to inspect your design

## Slide 27: Sources of truth vs Inventory
An inventory describes what you have
  Like counting how many tomato sauce cans you have in your shelves
  (After the facts)
A source of truth describes what should happen
  Like making an order of tomato sauce cans
  (Before the facts)
There might be disagreement
  You might want to inventory only what is active [for instance because you alert on it]
  Might be that what you have is not what you want [and you want to know!]
  Correct lifecycle management and processes helps clarifying

## Slide 28: There are no specials…
you need a feature that was not planned.
you have to do things differently to avoid hitting a bug.
you have to adapt to the other end of the cable
DESIGN IS ANYWAY FLUID

## Slide 29: There are no specials…
you need a feature that was not planned.
you have to do things differently to avoid hitting a bug.
you have to adapt to the other end of the cable
What is surely not design and so not truth:
Anything named “TEMP_*/TEST_*”
Anything related with debugging/troubleshooting.
DESIGN IS ANYWAY FLUID

## Slide 30: Enough talking, let’s see it in action!