## Slide 1
dCache & DMF:
tape at SURFsara
DMF
  (slides stolen from Jurriaan Saathof)
How dCache talks to DMF (Onno)
Atlas tape caroussel (slides stolen from Ron Trompert)
Presentation: Onno Zweers onno.Zweers@surfsara.nl
Hepix Barcelona 2018

## Slide 2: Data Preservation Services @ SURFsara
Data services
Jurriaan Saathof
Systems Expert

## Slide 3: Hierarchal Storage Management
Based on DMF by SGI
Complete filesystem view
Low cost storage media
      Disk to tape
Only data blocks
      Inodes remain on disk
Policies
      Filesize
      File age / last access time
Automated process
Queueing
Jurriaan Saathof– Data Preservation Services @ SURFsara

## Slide 4: Overview DMF
Jurriaan Saathof – Data Preservation Services @ SURFsara
CXFS filesystem
Tapedrives
DMF server (DB)
Data movers
Tape movers
SAN
To dCache

## Slide 5: Hardware
Jurriaan Saathof – Data Preservation Services @ SURFsara
Hardware (focus on LOFAR project, shared system)
4 data movers (shared with Grid projects)
        10GE, 4x FC8 (2x disk, 2x tape)
        Will be upgraded to 40GE, 8x FC16 @ Q4 2017
11 tapemovers (shared by all)
        8x FC16 (4x disk, 4x tape)
79TB filesystem (dedicated for LOFAR)
        12x 8+2 RAID6 LUN (120 disks, dedicated hardware controllers, 8x FC16)
        3x 4-disk stripe
        Inodes on SSD
10x T10000-D tapedrives configured (out of 34, shared by all)
        @252MB/s (native)
        8x reserved for writing, 2x always available for reading

## Slide 6: I/O Performance (LOFAR filesystem)
Jurriaan Saathof – Data Preservation Services @ SURFsara

## Slide 7: Automated Cartridge System
Jurriaan Saathof – Data Preservation Services @ SURFsara

## Slide 8: Automated Cartridge System (2)
Each library up to:
10000 slots
64 drives
8 robots
@SURFsara:
2 libraries
25 drives each
4 robots each
Jurriaan Saathof – Data Preservation Services @ SURFsara

## Slide 9
Two StorageTek tape libraries, 10k slots each
  Separate buildings
Data blocks can be on tape or cached on CXFS
iNodes of CXFS filesystem remain on SSDs
Small files remain on CXFS
Replicas
  HEP & Lofar: 1 copy
  Other: 2 copies, spread among 2 libraries
Migrating to LTO-8, 12 TB per cartridge
Some more facts

## Slide 10
An HSM script `dmfcp.sh` enables dCache to copy data to and from tape.
  put
    hpn-scp file from pool dir to a data mover node node
    check adler32 checksum
    If success, exit 0 to let dCache know it succeeded, and return the tape file name
  get
    dmstat on CXFS node to check the file status
    dmget to request copy from tape to CXFS
    repeat until status is online (on CXFS)
    hpn-scp copy file to the dCche pool dir
    exit code success: dCache will calculate the checksum and update location info
  delete
    hpn-ssh data-mover-node “rm -rf”
How dCache talks to DMF (1/3)

## Slide 11
Pitfall: exit codes are essential not to lose data.
How dCache talks to DMF (2/3)
scp
result=$?
scp | logger
result=${PIPESTATUS[0]}

## Slide 12
How dCache talks to DMF (3/3)
dCache pool
DMF
dCache SRM

## Slide 13
ATLAS tape caroussel @ NL-T1
Slides: Ron Trompert
Presentation: Onno Zweers
Hepix Barcelona 2018 – BoF tape session

## Slide 14
ATLAS tape caroussel @ NL-T1
Setup
DMF

## Slide 15
ATLAS tape caroussel @ NL-T1
10 tape drives T10KD
16 stage pool nodes (8.3TB-14.7TB per node) which do 100 stage requests concurrently each (the rest is queued by dCache)
We have added an extra 90TB to hold the complete dataset on the stage pools
The more concurrent stage requests DMF gets, the better because the more efficient DMF can schedule staging

## Slide 16
ATLAS tape caroussel @NL-T1
Basically left the config alone, but…..
We had a bumpy start

## Slide 17
ATLAS tape caroussel @NL-T1
Setting srmmanager.request.get.max-requests = 30000 srmmanager.request.bring-online.max-inprogress = 30000 fixed it.
They were both 10000

## Slide 18
ATLAS tape caroussel @NL-T1
When copying data from stage pools to DATADISK we have discovered a config error causing a high load. (WebDAV transfers were not limited.) Fixed it.
Played around a bit with the 100 concurrent stage requests per pool but that did not make a noticeable difference.

## Slide 19
ATLAS tape caroussel @NL-T1
Staged at about 630MB/s on average
Remounts
  Sep 5: "avgtaperemounts": 4.79
  Sep 6: "avgtaperemounts": 4.73
  Sep 7: "avgtaperemounts": 3.91
  Sep 8: "avgtaperemounts": 2.57

## Slide 20
ATLAS tape caroussel @NL-T1

## Slide 22
ATLAS tape caroussel @NL-T1
To increase performance:
  More tape drives
  CXFS filesystem used by our tape backend from which dCache copies files needs to become faster. The more tape drives we get (and the more dCache pool nodes) the more I/O capacity of the file system is needed
  Thinking of NVMe-base storage (but nothing concrete yet)
It is maybe better to replace the polling mechanism by a mechanism where the pool is notified that a file is online

## Slide 23
ATLAS tape caroussel @NL-T1
It would be good to run the tests again
        See if a file is read from tape more than once→ should not happen
        Tuning number of concurrent stage requests and read operations from CXFS/DMF nodes to optimize throughput

## Slide 24
Thank you